## Slide 1
March 10, 2026
1.
Presented by
Johnny Drahos, Environmental Scientist
Bureau of Safe Drinking Water
Revised Total Coliform Rule: Coliform Assessments
RCAC Water and Wastewater Conference
Nevada Division of
Environmental Protection

## Slide 2
Presentation Overview
Coliforms: What they are and why we care about them
Coliform Assessments:
  When they occur
  How to complete them
  How to avoid them in the first place

## Slide 3
Coliform explained
      Pathogens abound
        Bacteria, parasites, virus
      Bacteria – Coliform can be easily identified
        Indicator of potential contamination
      All species of coliform = total coliform
        Found in soil (includes dust in the wind)
        Found in surface water
        Found in feces of warm-blooded animals
        Should not be in closed drinking water systems

## Slide 4
  Total coliform = Environmental contamination
  Fecal coliform + E. Coli = Fecal contamination
  E. Coli = Fecal contamination + potential of illness
  E. coli 0157:H7 = Most common strain to cause illness/death
Coliform Explained

## Slide 5
Lorem Pisom
All Species of Coliform = Total Coliform
  Not distributed equally
  Suspended
  Sample 100 ml
  May not be in every sample
Detection indicates potential contamination
Why coliform is not in every sample

## Slide 6: Why coliform is not in every sample
Photo taken and owned by NDCNR, permission granted to NDEP

## Slide 7
Coliforms = proxy for bacterial contamination
Distribution systems serve either treated water or groundwater that does not require treatment
Either way, no coliforms should be present unless there is an open pathway for contamination to enter the system
Detecting coliform indicates potential contamination
More likely to detect coliform than e coli., regardless of if e coli. is also present.
Acts as a warning that gives water systems time to respond before it’s too late and adverse health effects are realized
Why sample total coliform when E Coli is the concern???

## Slide 8
13.
Routine coliform sample is TC+, EC-
This triggers repeat samples to be collected
  3 distribution system samples (original sample location, 1 sample upstream, 1 sample downstream)
  Source monitoring for any groundwater source that fed water to part of system that had coliform detection
*These “repeats” must be collected within 24hrs of learning of the original TC+ sample!!!
Contamination has likely occurred.
Triggering Assessments

## Slide 9
13.
Level 1 Assessment
Coliform Detections:
  Routine Compliance Sample & one or more Repeat Samples TC+ or >5% of Monthly Samples TC+
  No E. coli detected
  No Assessment in the past 12 rolling months
  OR
Failure to collect required repeat samples (or failure to collect within the required 24hr timeframe)
Contamination has likely occurred.
Triggering Assessments

## Slide 10
13.
Level 2 Assessment
Coliform Detections:
  Routine Compliance Sample & one or more Repeat Samples
AND
  Previous Assessment in the past 12 months
OR
E. coli detected in one or more samples
  Routine sample TC+EC+/ Repeat sample TC+EC+
  Routine sample TC+EC-/ Repeat sample TC+EC+
  Routine sample TC+EC+/ Repeat sample TC+EC-
Contamination has likely occurred.
Triggering Assessments

## Slide 11: Assessment Triggers 40 CFR 141.859
We loren i[sskdf fslfeiof test carwd sffielsff key trds that dfemand sfur attsensfftionf loren sopurfs.
We loren i[sskdf fslfeiof test carwd sffielsff key trds that dfemand sfur attsensfftionf loren sopurfs..
We loren i[sskdf fslfeiof test carwd sffielsff key trds that dfemand sfur attsensfftionf loren sopurfs.

## Slide 12
PWS must ensure Assessments are conducted
“Systems must ensure that Level 1 and 2 assessments are conducted in order to identify the possible presence of sanitary defects and defects in distribution system coliform monitoring practices. Level 2 assessments must be conducted by parties approved by the State”
If you think you have triggered an assessment, reach out to your regulators.
If your regulating agency does not catch the assessment trigger until after the due date, the water system is in violation for failure to complete it
Water System Responsibilities

## Slide 13
Conducting a Level 1 Assessment
Diverse Destinations
Lorem ipsum dolor sit amet conse adipiscing elit nullam felis mamus sit.
Responsible Recreation
Lorem ipsum dolor sit amet conse adipiscing elit nullam felis mamus sit.
Outdoor Adventure
Lorem ipsum dolor sit amet conse adipiscing elit nullam felis mamus sit.

## Slide 14: Conducting a Level 1 Assessment
  Checklist and summary letter go out
  Gather information
    Where was coliform detected?
    Distribution and/or source
    Troubleshoot/identify likely causes of coliform detection
    Take steps to correct any defects
    Often non-compliance samples need to be taken
  Complete the paperwork; collect photos of any repairs
  Submit finished form to Regulator within 30 days of trigger.

## Slide 15
Level 1 Assessment Findings
  Most common findings from L1 Assessments:
    Loss of pressure
    Not disinfecting
    Improper sampling
    Weather
    Unknown
  *there is not always an obvious explanation, reach out to your regulator if you are unsure how to proceed

## Slide 16
13.
Level 2 Assessment
Coliform Detections:
  Routine Compliance Sample & one or more Repeat Samples
AND
  Previous Assessment in the past 12 months
OR
E. coli detected in one or more samples
  Routine sample TC+EC+/ Repeat sample TC+EC+
  Routine sample TC+EC-/ Repeat sample TC+EC+
  Routine sample TC+EC+/ Repeat sample TC+EC-
Contamination has likely occurred.
Triggering Assessments

## Slide 17: Conducting a Level 2 Assessment
  If E. coli positive MCL Violation Letter is sent
    Public notice is required within 24 hours
  Site visit is scheduled with Regulator
  Site visit – Focus on identifying source of contamination and determining corrective actions necessary to resolve it
  Gather information
    Where were coliforms detected?
    Flow of positives within system
    Take steps to correct any defects
  Complete any Sanitary Defects found
  Submit the Assessment response to Regulator within 30 days of trigger

## Slide 18
Conducting a Level 2 Assessment
Templates are available on the NDEP website for public use:
Emergency Coliform Phone: 775-434-5233
Nevada Spill Hotline: 888-331-6337

## Slide 19
Level 2 Assessment Findings
  Most common findings from L1 Assessments:
    Loss of pressure
    Not disinfecting
    Improper sampling
    Source contamination
    Unknown

## Slide 20: How to Prevent an Assessment
Sample Collection
  Disinfection
  Flushing
  Sampling Procedure
  Using best judgement
  Selection of sample sites
Periodic System Inspection
  Distribution System
  Storage
  Treatment
  Sources
  Be aware of pressure losses

## Slide 21: How to Prevent an Assessment
  Follow your RTCR Sampling plan
  Use non-compliance samples to your advantage
  Ensure chain of custody directs labs to reach out to the correct staff for reporting coliform detections
  Ensure regulating agency has up to date contact info
  Correct sanitary survey deficiencies in a timely manner
  Sample early in the monitoring period, delay sampling if conditions are unideal (e.g. windy days)
6.

## Slide 22: Questions?
Johnny Drahos - BSDW
Nevada Division of Environmental Protection
Phone: 775-687-9559
Email: jdrahos@ndep.nv.gov